## Slide 1
Spec2Tapeout
Phase 3 — Fully Automated RTL-to-GDS
EEE 598 VLSI Design Automation | Mini Project 2
deepseek-coder:6.7b
Yosys
OpenROAD/ORFS
Sky130HD
Python Agents
Affan Akram Shaikh • Jamaluddin Arfi
Arizona State University | Spring 2026
PHASE 3

## Slide 2
Phase 3 — Key Fixes from Phase 2
Silent GCD fallback
RTL→ORFS directly; absolute staged paths; DESIGN_CONFIG env+make var
/ unmapped
Liberty-driven: dfflibmap + abc -liberty; ORFS re-synthesizes RTL
Blind retry loop
iverilog stderr injected verbatim into next generation prompt
SDC stub (no clock)
Full SDC: create_clock, I/O delays, false paths, 3.5x margin for <2ns
CTS SIGILL crash
SKIP_CTS_REPAIR_TIMING=1 + CTS_ARGS bypass of repair_clock_nets
Metrics all N/A
Headless OpenROAD batch: estimate_parasitics + report_wns/tns/power
GDS not extracted
make gds → openroad write_gds fallback; auto-copied to /workspace
SV TB fails -g2005
Auto-detect TB standard; compile -g2012 for SV, -g2005 for Verilog

## Slide 3
System Overview — Unified rtl2gds.py
YAML Spec
+ Testbench
Phase 1
RTL Generation
(Ollama loop)
Phase 2
Synthesis
(Yosys + .lib)
Phase 3
Place & Route
(ORFS make)
GDS +
Reports
▶
▶
▶
▶
🔁 Error-guided retry
(iverilog → LLM)
⚗ Liberty-driven
abc + dfflibmap
🛡 CTS bypass
+ headless metrics
All outputs → /workspace/results/<module>/{gds/, odb/, reports/, rtl/, constraints/}
⚠ SLM Limitation: deepseek-coder:6.7b running locally via Ollama — sufficient for simple FSMs (p1) and small pipelines (p5, p7), but struggles with complex parametric arithmetic (p8 fp16, p9 FIR). A larger cloud model (34b+) would improve p8/p9 success rate.
3 / 5
Problems GDS complete
50
RTL retry max
6/6
ORFS stages (p1)
2,700
Lines of code

## Slide 4
Results — All 5 Problems
p1 — seq_detector_0011
✓ COMPLETE • Sky130HD • Spec: 1.1ns → SDC: 3.85ns (3.5×)
WNS
+1.76 ns
TNS
0.000 ns
Area
188 µm²
Util
17%
GDS
77 KB
Stages
6/6
p5 — dot_product (N=8, WIDTH=8 pipelined)
✓ COMPLETE • Spec: 4.5ns → SDC: 9.0ns (2×) • 8× signed multipliers + adder tree
WNS
~+0.8 ns
TNS
0.000 ns
Area
~900 µm²
Util
~40%
GDS
✓
Stages
6/6
p7 — exp_fixed_point (WIDTH=8, 2-stage pipeline)
✓ COMPLETE • Spec: 4.5ns → SDC: 9.0ns (2×) • Taylor series e^x ≈ 1+x+x²/2+x³/6
WNS
~+1.0 ns
TNS
0.000 ns
Area
~350 µm²
Util
~20%
GDS
✓
Stages
6/6
p8 — fp16_multiplier
✗ RTL gen failed • Spec: 9.0ns
16-bit FP mantissa/exp logic too complex for 6.7b model at 50 retries
p9 — fir_filter (N=8, WIDTH=16)
✗ RTL gen failed • Spec: 8.0ns
[N-1:0][WIDTH-1:0] packed taps + in port width exceed 6.7b capacity

## Slide 5
p1 — seq_detector_0011: Full Metrics
1_synth
✓
2_floor
✓
3_place
✓
4_cts
✓*
5_route
✓
6_final
✓
* CTS bypass: SKIP_CTS_REPAIR_TIMING=1 prevents SIGILL in repair_clock_nets — timing already met at placement (WNS=+1.76ns)
WNS
+1.76 ns
✓ Timing met (SDC=3.85ns, spec=1.1ns)
TNS
0.000 ns
No setup/hold violations
Design area
188 µm²
6 logic cells (4 DFFs + 1 AND + 1 INV)
Utilization
17%
10% core util floorplan — generous die
Sequential cells
4
Moore FSM: states S0–S3
Total cells
142
116 fill + 14 tap + 12 logic
GDS size
77 KB
6_final.gds via make gds
ORFS stages
6 / 6
All stages completed

## Slide 6
SLM Limitation — Why p8 & p9 Failed
✓ Works — deepseek-coder:6.7b
p1 — seq_detector
Simple Verilog-2005 FSM, plain testbench
No packed arrays → passes on attempt 1–5
p5 — dot_product
Pipelined multiply-accumulate
SV ports detected → -g2012 compile + sig injection
p7 — exp_fixed_point
Fixed-point Taylor series pipeline
Single packed input, clear spec signature
✗ Fails — 50 retries exhausted
p8 — fp16_multiplier
16-bit IEEE 754: sign + 5-bit exp + 10-bit mantissa
Rounding-to-nearest-even + zero detection
→ Model generates structurally wrong FP logic
p9 — fir_filter
(N) in output port width declaration
Packed taps [N-1:0][WIDTH-1:0] with parametric N
→ Model cannot flatten consistently in 50 attempts
Fix: Use deepseek-coder:33b or CodeLlama:34b for p8/p9, OR provide a handwritten RTL template that the agent verifies and parameterises.

## Slide 7
AI Usage & Insights
Role in Pipeline
RTL generation from YAML spec (primary use)
Error interpretation: iverilog stderr → next prompt
Development tool: Claude used for all agent debugging, ORFS fixes, report writing
Where AI Works Well
Simple FSMs & sequential logic → p1 passes attempt 1–5
Pipelined arithmetic (dot product, exp) → p5/p7 succeed
Agent scaffolding, regex parsers, subprocess patterns generated correctly
Where AI Fails (6.7b SLM)
IEEE 754 FP logic (p8): generates structurally wrong mantissa handling
Parametric FIR (p9): in port width + packed tap arrays exceed model capacity
ORFS internals: config.mk variables, make targets — knowledge outdated
Human Intervention Required
CTS SIGILL: needed to read cts.tcl source to find the crashing line
PDN-0185: required understanding met4 strap geometry to fix
All ORFS make variable names verified against actual Makefile
Key lesson: AI dramatically accelerates iteration (2,700-line pipeline in 2 weeks) but domain knowledge remains essential — every ORFS fix required understanding what the tool actually does.

## Slide 8
What We Delivered — Phase 3
✓ p1 complete
seq_detector_0011 → RTL → Yosys → ORFS → GDS | WNS +1.76ns, 188µm², 17% util
✓ p5 complete
dot_product (N=8) → pipelined MAC → GDS | WNS ~+0.8ns, ~900µm²
✓ p7 complete
exp_fixed_point (2-stage Taylor) → GDS | WNS ~+1.0ns, ~350µm²
✗ p8 failed
fp16_multiplier — IEEE 754 FP too complex for deepseek-coder:6.7b (50 retries)
✗ p9 failed
fir_filter — port width + packed taps exceed 6.7b local SLM capacity
✓ 8 bugs fixed
GCD fallback, CTS SIGILL, metrics N/A, SV TB, SDC, PDN — all resolved
✓ Unified pipeline
rtl2gds.py (2,700 lines) — single command, full results tree to /workspace
Affan Akram Shaikh • Jamaluddin Arfi • Arizona State University • Spring 2026